36,000 # GVWR C/C – BIDDER TO COMPLETE

## Delivered Price / Unit

Description                           		  	           US Dollars

NEW 2014 MODEL YEAR 36,000 # GVWR TRUCK CAB AND CHASSIS AS PER STATE OF NEW HAMPSHIRE SPECIFICATION #’S 2001-00 AND 2014-48 DOT																								$ ___________________

BIDDER TO COMPLETE

ADD FOR OPTIONS:

CAB TO AXLE DIMENSION 96”					$

CAB TO AXLE DIMENSION 108”					$

CAB TO AXLE DIMENSION 120”					$

SUBTRACT FOR OPTIONS:

REMOVE LEFT OR RIGHT FRONT DRIVER CONTROLLED OVERLOAD AIR BAG

($     			)

REMOVE SOFTWARE REQUIREMENT

($___________________)

ENGINE TYPE

MANUFACTURER/MODEL

## 55,000 # GVWR C/C – BIDDER TO COMPLETE

Description                           			  Delivered Price / Unit

NEW 2014 MODEL YEAR 36,000 # GVWR TRUCK CAB AND

CHASSIS AS PER STATE OF NEW HAMPSHIRE SPECIFICATION #’S

2001-00 AND 2014-48 DOT									$

ADD FOR UPGRADES / OPTIONS:

- CAB TO AXLE DIMENSION 138”				 	 		$

- CAB TO AXLE DIMENSION 150”				  	 		$

- ENGINE UPGRADE ADDITIONAL CHARGE 			   	 		$

ADD FOR ENGINE UPGRADE OPTIONS

- INTERNATIONAL MAX FORCE 13, 450 HP @1,700 RPM, 1,550 FT LB @ 1,000 RPM,	$

- CUMMINS ISX 15 450 HP @ 1,700 RPM, 1,650 FT LB @ 1,200 RPM			$

- MACK MP3 MAXI DYNE 455 HP @ 1,500 RPM 1,650 FT LB @ 1,200 RPM		$

- DETROIT DIESEL DD13 12.8L 450 HP @ 1800 RPM, 1,650 FT LB @ 1100 RPM		$

- PACCAR 12.9L MX340, 455 HP @1700 RPM, 1650 FT LB @1000 RPM			$

ENGINE TYPE

MANUFACTURER/MODEL

DEDUCT FOR OPTIONS:

- REMOVE LEFT OR RIGHT FRONT DRIVER CONTROLLED OVERLOAD AIR BAG   	($ 			)

- REMOVE SOFTWARE REQUIREMENT						             ($ 			)

ADD / DEDUCT FOR REQUESTED EQUIPMENT SUBSTITUTION PACKAGE

ADD: 		1 EACH   ALLISON HOSE KIT #329130-1X.

1 EACH   MFG. CHELSEA PTO Model 890HAFJW-B5AF.

I EACH    MFG PARKER Model #PGP330B197***AB20-98KPAB20-1 double sealed Tandem pump.						                        OR,

1 EACH   MFG PERMCO Model #P2100D086NGX12087AZA20-1 double sealed Tandem pump.

REMOVE 	1 EACH   MFG  CHELSEA WET SPLINE MODEL #277XBFJW-B5AF  TO INCLUDE HOSE KIT #329130-1X TO INCLUDE HYDRAULIC PUMP PARKER PUMP # MODEL #324-9110-448, ( PART OF STANDARD SPECIFICATION, SEE #55,000 SPEC – TRANSMISSION **

$ 	         OR   ($ _________)

DELIVERY		DAYS AFTER RECEIPT OF PURCHASE ORDER DELIVERY NOT TO EXCEED 150 CALENDAR DAYS ARO

PAGE 1 OF 4

STATE OF NEW HAMPSHIRE

NH SPECIFICATION NO. 2014-48 DOT

DEPARTMENT OF ADMINISTRATIVE SERVICES			                                                     October 15, 2013

BUREAU OF PURCHASE AND PROPERTY

## STANDARD SPECIFICATION – 2014 TRUCK, CAB & CHASSIS –36,000 #

GROSS VEHICLE WEIGHT RATING 	MINIMUM 36,000 POUNDS

CAB

- CONVENTIONAL 3-POINT ACCESS CAB, ADDITIONAL GRAB HANDLE TO BE MOUNTED ON THE EXTERIOR OF DRIVER’S SIDE CAB CORNER

- BUTTERFLY HOOD OR HATCHES TO ALL SERVICE POINTS

- STATIONARY GRILLE

- DUAL FACTORY INSTALLED 7” FENDER MOUNTED HEATED CONVEX MIRRORS

- ONE PIECE WINDSHIELD

- DRIVER AND PASSENGER DOOR OPERATING VENT WINDOWS OR FACTORY INSTALLED VENT SHADES

- CAB NOISE SUPPRESSION ON INSIDE OF FIREWALL AND ENGINE COMPARTMENT AND ADDITIONAL FRONT DIRECTIONAL TURN SIGNAL LIGHTS TO BE MOUNTED ON TOP OF OR IN FENDERS.

- INNER FENDER SPLASH GUARDS

- CAB SUSPENSION TO BE AIR BAG TYPE

- AUX.  HEADLIGHT HARNESS SWITCHED IN CAB TO FRONT OF VEHICLE FOR PLOW LIGHTS & TURN SIGNALS CONSISTING OF THREE (3) EA. # 1157 BULBS ON EACH SIDE

- RUBBER FENDER EXTENSIONS

- KEYED ALIKE LOCKS. OUTSIDE AIR / TEMPERATURE MONITOR

- WIPER FORCED TO INTERMITTENT WHEN SERVICE BRAKE IS APPLIED

.

CAB HEIGHT  			                MINIMUM 59-1/2” (EXTERIOR FRAME TO TOP OF CAB)

CAB – AXLE DIMENSION		                84” USABLE

BBC DIMENSION                                                107” – 114”

TRANSMISSION

- AUTOMATIC – 3500 RDS, FIVE SPEED, PRE SELECT FOR SELECT ONE (1) GEAR DOWN VARIABLE COMPRESSION ENGINE BRAKE 3RD GEAR HOLD WITHOUT (LBSS) LOAD BASED SHIFT SCHEDULE

- RIGHT SIDE DASH MOUNTED TOUCH PAD CONTROL

- AUTO NEUTRAL WHEN PARKING BRAKE IS APPLIED

- INTEGRAL OIL LEVEL SENSOR

- TES 295 APPROVED SYNTHETIC FLUID

- EXTENDED TRANSMISSION WARRANTY COVERAGE- PARTS, LABOR AND TOWING FOR FIVE (5) YEARS, UNLIMITED MILEAGE FROM IN-SERVICE DATE (DETERMINED BY STATE)

- AUXILIARY COOLING

PTO AND PUMP

- ALSO INCLUDED: DRIVERS SIDE INSTALLED CHELSEA WET SPLINE PTO MODEL #277XGFJW-B5AF TO INCLUDE HOSE KIT #329130-1 AND A HYDRAULIC PUMP THAT SHALL BE A PARKER MODEL #324-9110-448

- A FACTORY IN DASH ILLUMINATED SWITCH SHALL BE INSTALLED, LABELED “PTO”, A SEPARATE INDICATOR LIGHT INSTALLED IN THE DASH AT A LOCATION DETERMINED BY THE NHDOT, FOR THE OPERATION OF THE PTO.  THE SOURCE OF POWER SHALL NOT BE THROUGH THE VEHICLE’S ECM

COOLING

  - HEAVY DUTY WITH LONG LIFE ANTIFREEZE AND A COOLANT RECOVERY TANK

AIR CONDITIONING TO BE FACTORY INSTALLED

BATTERY & ALTERNATOR

- THREE (3)-BATTERIES EACH HAVING 180 AMP HOUR RATING (9N COMBINATION) WITH 2,775 CCA

- DELCO 24 SI OR LEECE-NEVILLE 160 AMP ALTERNATOR

- BATTERY BOX MOUNTED FOR CLEAN C.A. IF AVAILABLE

BRAKES

- POWER - ABS, ALL WHEEL, AIR BRAKES, CAM

- AIR BRAKE PROVISIONS TO REAR OF CHASSIS

- COMPRESSOR CAPACITY  (13 CUBIC FT.  MIN.)

- AUTOMATIC SLACK ADJUSTERS FRONT AND REAR

- ANCHORLOCK PARKING BRAKE (OR EQUIVALENT), MGM BRAND OR MERITOR SEALED LONG STROKE CHAMBERS WITH STAINLESS STEEL PINS

###### PAGE 2 OF 4

## STANDARD SPECIFICATION – 2014 TRUCK, CAB & CHASSIS 36,000# - CONTINUED

- ADIP AIR DRYER LOCATED ON OUTSIDE OF FRAME

- DUST SHIELDS – ALL WHEELS

ENGINE – DIESEL

- INTERNATIONAL DT466E 285 HP @ 2,200 RPM, 860 FT LB @ 1,300 RPM

- CUMMINS ISL 8.9 300 HP @ 2,200 RPM, 860 FT LB @ 1,400 RPM

- PACCAR PX-9 300 HP @ 2200 RPM, 860 FT LB @ 1400 RPM

- SHALL INCLUDE ENGINE BRAKE

- FUEL/ WATER SEPARATOR LOCATED ON OUTSIDE OF FRAME OR UNDER HOOD

- FUEL FILTER,

- 2 POSITION PROGRAMMABLE STEP UP THROTTLE

- AUDIBLE ALARM

- STEEL OR CAST ALUMINUM SUMP OIL PAN

EXTENDED ENGINE WARRANTY

  - A SEVEN (7) YEAR, OR 7,500 HOUR 100% PARTS, LABOR AND TOWING WARRANTY SHALL COVER COMPUTERS,  MODULES, ELECTRICAL CONNECTIONS, CONNECTORS, WIRING HARNESSES, INJECTORS, INJECTOR LINES, TURBOS, WATER PUMPS, FUEL FILTER ASSY, STARTERS, CLUTCH FANS, ALTERNATORS, OIL AND FUEL PRESSURE PUMPS, OIL AND WATER SEALS, ALL ENGINE MECHANICAL PARTS AND EMISSION RELATED COMPONENTS.   MAINTENANCE COMPONENTS SUCH AS BELTS, HOSES AND FILTERS ARE EXCLUDED.  WARRANTIES TO BEGIN ON THE IN-SERVICE DATE OF THE CHASSIS AND IS DETERMINED BY THE STATE.

STEERING

- HYDRAULIC POWER STEERING WITH DUAL STEERING BOXES

- STEERING WHEEL DIAMETER MINIMUM 16” WITH TILT ADJUSTABLE COLUMN

ELECTRICAL

- ALL ELECTRONIC CONTROLLERS, EXCEPT ENGINE ECM, TO BE LOCATED IN THE CAB NOT TO INTERFERE WITH SPACE BETWEEN SEATS,

- SINGLE HARNESS IN TRUCK FOR VEHICLE SPEED AND GROUND SPEED SENSING.

- MINIMUM OF SIX OPTIONAL IN-DASH SWITCHES, KEY POWER, TERMINATING @ FIREWALL, LABELED “PTO”, “SPARE”,  “SPREAD”

- AUX. PARK BRAKE ALARM

- HEADLIGHTS ON W/WIPERS

- A DEDICATED WIRE FOR A TWO-WAY RADIO, FUSED AT 20 AMPS TERMINATING UNDER DASH

- CB RADIO PREP PACKAGE WITH 2 FT. SPRING MOUNTED ANTENNA (S)

- 12V ACCESSORY PORT

- PRE-WIRED CIRCUIT FOR ELECTRIC TRAILER BRAKES

- SEVEN WIRE HARNESS TO REAR OF FRAME FOR A TWO (2) LIGHT (COMBINATION STOP/TURN/TAIL) SYSTEM WITH A PACKARD CONNECTOR #12124685 & #12124686 INSTALLED AND A SUPPLIED PHILLIPS STA-DRY PLUG ASSY PART # 48NA33-036

SUSPENSION

FRONT AXLE

- 16,000 # WITH WET TYPE OIL SEALS

FRONT SPRINGS

- 16,000 # COMBINED RATING @ GROUND, MULTI-LEAF, SEMI-ELLIPTIC

- NOTE: IF SETBACK FRONT AXLE IS OFFERED, ADD 2,000 # TO MAIN SPRING/AXLE GROUND RATING

- RIGHT OR LEFT FRONT (AS SPECIFIED) DRIVER CONTROLLED AIR BAG OVERLOAD

REAR AXLE

  - 23,000 # EATON, MERITOR OR SPICER, MINIMUM 18” RING GEAR

  - DRIVER CONTROLLED LOCKING DIFFERENTIAL

  - SINGLE SPEED AXLE (RATIO TO BE DETERMINED BY USING AGENCY)

REAR SPRINGS

- 30,000 # TOTAL COMBINED RATING @ GROUND, INCLUDES REAR MAIN MULTI LEAF,  AND 2,250 # AUXILIARY SPRINGS

DRIVELINE

- SPICER SERIES 1710 SERIES

### PAGE 3 OF 4

## STANDARD SPECIFICATION – 2014 TRUCK, CAB & CHASSIS 36,000# - CONTINUED

TIRES: TYPE, WHEEL/TIRE SIZE

- SEVEN (7) – HEAVY DUTY ACCURIDE  24.5” X 8.25”, POWDER COATED STEEL, HUB PILOTED, 0.472” DISC WHEELS WITH GUARDS FRONT & REAR

- SIX (6) – 11R24.5 (H)  TUBELESS RADIALS

- WHEEL WRENCH AND HANDLE

ACCEPTABLE BRAND TIRES

FRONT

- GOODYEAR G287 MSA OR MICHELIN XZY-3

REAR

- GOODYEAR G282 MSD OR MICHELIN XDS-2

FRAME

- HEAT TREATED ALLOY STEEL FRAME WITH MINIMUM YIELD STRENGTH OF 120,000 PSI AND MINIMUM SECTION MODULUS

OF 20.6

- 1 PIECE, FULL DEPTH FRAME TO EXTEND A MINIMUM OF 12” BEYOND FRONT OF GRILLE.

- AF-MINIMUM 48”

- BOTH OUTSIDE FRAME RAILS TO BE FREE OF OBSTRUCTIONS FOR TWENTY FOUR (24) INCHES BEHIND THE CAB TO ALLOW ROOM FOR MOUNTING A WING CABINET

- MINIMAL OBSTRUCTIONS FOR NEXT THIRTY (30) INCHES FOR PIPE BRACES

INSTRUMENTS/CONTROLS

- SPEEDOMETER, TACHOMETER, AMMETER/VOLT-METER, FUEL GAUGE (S), OIL PRESSURE GAUGE, TEMPERATURE GAUGE

AND AIR PRESSURE GAUGE

- ALL NECESSARY ELECTRICAL SWITCHES

- HOUR METER, ACTUATED BY ENGINE OPERATION

- DASH MOUNTED AIR RESTRICTION INDICATOR

FUEL SUPPLY

- STAINLESS STEEL OR ALUMINUM TANK WITH STAINLESS STEEL STRAPS HAVING A MINIMUM CAPACITY OF 70 GALLONS

- STEP TYPE FUEL TANK. NOT TO EXCEED 4” BEYOND REAR OF CAB

EXHAUST SYSTEM

- HORIZONTAL, VERTICAL  (OR COMBINATION) MUFFLER SYSTEM SHALL BE CONFIGURED NOT TO INTERFERE WITH PTO’S OR HYDRAULIC CABLES.

- STACK (INCLUDING 90 DEGREE TURN OUT) MUST NOT EXTEND ABOVE TOP OF CAB. AND NOT TO EXCEED 4” BEYOND REAR OF CAB

PAINT

- CLEAR COAT OMAHA ORANGE (SAME AS DUPONT DULUX 93-082) LEAD FREE

- NOTE:  SEE INDEPENDENT PAINT TESTING REQUIREMENTS AS PART OF THIS SPECIFICATION

RADIO/SPEAKERS (FACTORY)

- AM/FM WITH WEATHER BAND

SEATS-DRIVER/PASSENGER

- BUCKET, AIR SUSPENSION, HIGH BACK, HEAD REST, DRIVER’S ARM REST (RH) (NATIONAL CUSHION-AIRE OR EQUAL), HD CLOTH MORDURA, MILLIKEN (NGV) OR EQUAL.

FLOOR COVER

- VINYL WITH FACTORY RUBBER AUXILIARY MATS

LIGHTING, REQUIRED

- DAYTIME RUNNING, PRE-TRIP INSPECTION LIGHT TEST

MIRRORS, OUTSIDE RIGHT AND LEFT

- HEATED 6” X 15” EXTENDING TO 96” WITH A HEATED 7” CONVEX MIRROR

- PASSENGER SIDE “LOOK DOWN” CONVEX MIRROR

BUMPERS -FRONT

- NONE REQUIRED

PAGE 4 OF 4

## STANDARD  SPECIFICATION – 2014 TRUCK, CAB & CHASSIS 36,000# - CONTINUED

BACK UP ALARM

  - ELECTRIC

HORNS

- AIR AND ELECTRIC – DUAL NOTE, BOTH MOUNTED UNDER CAB

TOW PACKAGE

- TRAILER TOW PACKAGE SHALL BE PROVIDED AND INCLUDE TRAILER LIGHT PACKAGE, HAND OPERATED CONTROL VALVE, AND AIR LINES TO REAR OF FRAME

SOFTWARE

- DIAGNOSTIC SOFTWARE AND ALL REQUIRED LAPTOP COMPUTER CABLES AND OR CONNECTIONS FOR DIAGNOSIS OF ENGINE (INCLUDING KEY ON AND KEY OFF TEST, CYLINDER CUT OUT TEST, INJECTOR DISABLE TEST), CHASSIS & ELECTRICAL SYSTEM, AND ABS SYSTEM. LATEST VERSION OF ALLISON TRANSMISSION SOFTWARE SHALL BE PROVIDED FOR PROGRAMMING WITH ONE DAY ON SITE (DOT) PROGRAMMING INSTRUCTION.

- ALL SOFTWARE TO INCLUDE FREE UPDATES AND RENEWALS OF ALL SUBSCRIPTIONS FOR A PERIOD OF TEN (10) YEARS BEYOND MODEL YEAR. THIS SPECIFICATION SHALL REQUIRE A QUANTITY OF NINE ( 9 EACH ) COMPLETE SETS OF THE ABOVE SOFTWARE BE SUPPLIED AND DELIVERED TO NHDOT MECHANICAL SERVICES AS PART OF THIS SOLICITATION AND INCLUDED IN THE UNIT COST.

SYSTEMS CALIBRATIONS

UPON FINAL AWARD, THE SUCCESSFUL VENDOR WILL PRESENT A COMPLETE LIST OF DEFAULT ENGINE, ELECTRICAL, FUEL AND TRANSMISSION SYSTEM CALIBRATIONS FOR REVIEW AND ADJUSTMENT WITH THE END USER

SERVICE AND PARTS MANUALS

- FOR THE LIFE OF THE VEHICLE (S), THE AWARDED BIDDER SHALL PROVIDE WEB BASED ACCESS TO ALL TRUCK-SPECIFIC SERVICE MANUALS, TECHNICAL SPECIFICATIONS AND PARTS CATALOGS FOR A MINIMUM OF ELEVEN (11) NHDOT VEHICLE MAINTENANCE LOCATIONS.

APPLICATION: THIS SPECIFICATION COVERS THE STATE OF NEW HAMPSHIRE’S MINIMUM REQUIREMENT FOR A VOCATIONAL CAB & CHASSIS, INTENDED FOR THE SOLE PURPOSE OF PLOWING, SANDING AND OTHER HIGHWAY MAINTENANCE OPERATIONS. TO FACILITATE THE MOUNTING OF PLOW EQUIPMENT, AMPLE SPACE MUST BE AVAILABLE FOR LEFT AND RIGHT POWER TAKE OFFS. CLEAR SPACE BENEATH AND TO THE REAR OF THE CAB FOR HYDRAULIC CABLES AND WING CABINET.  ALL EXPOSED CONNECTIONS SHALL BE SEALED AND 100% WATER TIGHT.  THE MANUFACTURER WILL BE SOLELY RESPONSIBLE FOR MEETING THIS REQUIREMENT.

PAGE 1 OF 4

STATE OF NEW HAMPSHIRE

NH SPECIFICATION NO. 2014-50 DOT

DEPARTMENT OF ADMINISTRATIVE SERVICES					OCTOBER 15, 2013

BUREAU OF PURCHASE AND PROPERTY

## STANDARD SPECIFICATION –2014 TRUCK, CAB & CHASSIS –55,000 #

GROSS VEHICLE WEIGHT RATING  	MINIMUM 55,000 POUNDS

CAB

- CONVENTIONAL 3-POINT ACCESS CAB, ADDITIONAL GRAB HANDLE TO BE MOUNTED ON THE EXTERIOR OF DRIVER’S SIDE CAB CORNER

- BUTTERFLY HOOD OR HATCHES TO ALL SERVICE POINTS

- STATIONARY GRILLE

- DUAL FACTORY INSTALLED 7” FENDER MOUNTED HEATED CONVEX MIRRORS

- ONE PIECE WINDSHIELD

- DRIVER AND PASSENGER DOOR OPERATING VENT WINDOWS OR FACTORY INSTALLED VENT SHADES

- CAB NOISE SUPPRESSION ON INSIDE OF FIREWALL AND ENGINE COMPARTMENT

- ADDITIONAL FRONT DIRECTIONAL TURN SIGNAL LIGHTS TO BE MOUNTED ON TOP OF OR IN FENDERS

- INNER FENDER SPLASH GUARDS

- CAB SUSPENSION TO BE AIR BAG TYPE.

- AUX.  HEADLIGHT HARNESS SWITCHED IN CAB TO FRONT OF VEHICLE FOR PLOW LIGHTS & TURN SIGNALS CONSISTING OF THREE (3) EA. # 1157 BULBS ON EACH SIDE

- RUBBER FENDER EXTENSIONS

- KEYED ALIKE LOCKS

- OUTSIDE AIR / TEMPERATURE MONITOR

- WIPER FORCED TO INTERMITTENT WHEN SERVICE BRAKE IS APPLIED

CAB HEIGHT			                MINIMUM 59-1/2” (EXTERIOR FRAME TO TOP OF CAB)

CAB – TRUNION DIMENSION		MIN 120” TO MAX 126”

BBC DIMENSIONS		                MIN 105” TO MAX 117”

TRANSMISSION

- AUTOMATIC – 4500 RDS, SIX SPEED, PRE SELECT FOR SELECT ONE (1) GEAR DOWN VARIABLE COMPRESSION ENGINE BRAKE 3RD GEAR HOLD WITHOUT (LBSS) LOAD BASED SHIFT SCHEDULE

- RIGHT SIDE DASH MOUNTED TOUCH PAD CONTROL

- AUTO NEUTRAL WHEN PARKING BRAKE IS APPLIED

- INTEGRAL OIL LEVEL SENSOR

- TES 295 APPROVED SYNTHETIC FLUID

- EXTENDED TRANSMISSION WARRANTY COVERAGE- PARTS, LABOR AND TOWING FOR FIVE (5) YEARS, UNLIMITED MILEAGE FROM IN-SERVICE DATE (DETERMINED BY STATE)

- AUXILIARY COOLING

PTO AND PUMP

- ALSO INCLUDED: DRIVERS SIDE INSTALLED CHELSEA WET SPLINE PTO MODEL #277XBFJW-B5AF TO INCLUDE HOSE KIT #329130-1X AND  A HYDRAULIC PUMP THAT SHALL BE A PARKER PUMP # MODEL #324-9110-448

- A FACTORY IN DASH ILLUMINATED SWITCH SHALL BE INSTALLED, LABELED “PTO”, A SEPARATE INDICATOR LIGHT INSTALLED IN THE DASH AT A LOCATION DETERMINED BY THE NHDOT, FOR THE OPERATION OF THE PTO.  THE SOURCE OF POWER SHALL NOT BE THROUGH THE VEHICLE ECM

COOLING

- HEAVY DUTY WITH LONG LIFE ANTIFREEZE AND A COOLANT RECOVERY TANK

AIR CONDITIONING TO BE FACTORY INSTALLED

BATTERY & ALTERNATOR

- THREE (3), 12-VOLT-BATTERIES EACH HAVING 180 AMP HOUR RATING WITH 2775 CCA

- DELCO 28 SI , BOSCH  LH160, OR LEECE-NEVILLE 160 AMP ALTERNATOR WITH MINIMUM 25 AMP OUT @ 1,250 ALTERNATOR RPM

- BATTERY BOX MOUNTED FOR CLEAN C.A. IF AVAILABLE

BRAKES

- POWER - ABS, ALL WHEEL, AIR BRAKES, CAM

- AIR BRAKE PROVISIONS TO REAR OF CHASSIS

- COMPRESSOR CAPACITY  (13 CUBIC FT.  MIN.)

- AUTOMATIC SLACK ADJUSTERS FRONT AND REAR

PAGE 2 OF 4

STANDARD SPECIFICATION – 2014 TRUCK, CAB & CHASSIS 55,000# - CONTINUED

- ANCHORLOCK PARKING BRAKE (OR EQUIVALENT), MGM BRAND OR HALDEX SEALED LONG STROKE CHAMBERS WITH STAINLESS STEEL PINS

- ADIP AIR DRYER LOCATED ON OUTSIDE OF FRAME

  - DUST SHIELDS – ALL WHEELS

ENGINE – DIESEL

- MAX FORCE 13L, 410 HP @1,700 RPM, 1,450 FT LB @ 1,000 RPM

- CUMMINS ISX 12L, 400 HP @ 2,100 RPM, 1,450 FT LB @ 1,200 RPM

- MACK MP7- 405M MAXIDYNE, 405 HP @ 1,500 RPM 1,480 FT LB @ 1,200 RPM

- DETROIT DIESEL DD13, 12.8L, 410 HP @ 1800 RPM, 1,550 FT LB @ 1100 RPM

- PACCAR MX,13.0L, 405 HP @1900 RPM, 1450 FT LB @ 1100 RPM

- VARIABLE COMPRESSION ENGINE BRAKE

- FUEL/WATER SEPARATOR LOCATED ON OUTSIDE OF FRAME OR UNDER HOOD

- FUEL FILTER

- ENGINE BLOCK HEATER

- 2 POSITION PROGRAMMABLE STEP UP THROTTLE

- AUDIBLE ALARM

- STEEL OR CAST ALUMINUM SUMP OIL PAN

EXTENDED ENGINE WARRANTY

- A SEVEN (7) YEAR, OR 8,000 HOUR 100% PARTS, LABOR AND TOWING WARRANTY SHALL COVER COMPUTERS, MODULES, ELECTRICAL CONNECTIONS, CONNECTORS, WIRING HARNESSES, INJECTORS, INJECTOR LINES, TURBOS, FUEL FILTER ASSY, WATER PUMPS, STARTERS, CLUTCH FANS, ALTERNATORS, OIL AND FUEL PRESSURE PUMPS, OIL AND WATER SEALS, ALL ENGINE MECHANICAL PARTS AND EMISSION RELATED COMPONENTS.   MAINTENANCE COMPONENTS SUCH AS BELTS, HOSES AND FILTERS ARE EXCLUDED.  WARRANTIES TO BEGIN ON THE IN-SERVICE DATE OF THE CHASSIS AND IS DETERMINED BY THE STATE.

STEERING

- HYDRAULIC POWER STEERING WITH DUAL STEERING BOXES

- STEERING WHEEL DIAMETER MINIMUM 18” WITH TILT ADJUSTABLE COLUMN

ELECTRICAL

- ALL ELECTRONIC CONTROLLERS, EXCEPT ENGINE ECM, TO BE LOCATED IN THE CAB NOT TO INTERFERE WITH SPACE BETWEEN SEATS

- SINGLE HARNESS IN TRUCK FOR VEHICLE SPEED AND GROUND SPEED SENSING

- MINIMUM OF SIX OPTIONAL IN-DASH SWITCHES, KEY POWER, TERMINATING @ FIREWALL, LABELED “PTO”, “SPARE”,  “SPREAD”

- AUX PARK BRAKE ALARM

- HEADLIGHTS ON W/WIPERS

- A DEDICATED WIRE FOR A TWO-WAY RADIO, FUSED AT 20 AMPS TERMINATING UNDER DASH

- CB RADIO PREP PACKAGE WITH 2 FT. SPRING MOUNTED ANTENNA (S)

- 12V ACCESSORY PORT. PRE-WIRED CIRCUIT FOR ELECTRIC TRAILER BRAKES

- SEVEN WIRE HARNESS TO REAR OF FRAME FOR A FOUR (4) LIGHT (ALL RUNNING LIGHTS WITH SEPARATE STOP AND TURN SIGNAL) SYSTEM WITH A PACKARD CONNECTOR #12124685 & #12124686 INSTALLED AND A SUPPLIED PHILLIPS STA-DRY PLUG ASSY PART # 48NA33-036

SUSPENSION

FRONT AXLE

- 20,000 # WITH WET TYPE OIL SEALS

FRONT SPRINGS

- 20,000 # COMBINED RATING @ GROUND, MULTI-LEAF SEMI-ELLIPTIC

REAR AXLE

- 46,000 # DANA DD463P, MERITOR MT46-160P, MACK S462 AXLES (RATIO TO BE  DETERMINED BY USING AGENCY) HENDRICKSON           HMX-460-54 SUSPENSION

- MANUALLY CONTROLLED INTER-AXLE POWER DIVIDER LOCKOUT SHALL BE FURNISHED WITH EATON, MERITOR OR MACK             AXLES

- WARNING LIGHT TO BE PROVIDED TO INDICATE LOCKOUT ENGAGEMENT

- REARWARD TANDEM,DRIVER CONTROLLED DIFFERENTIAL LOCK

PAGE 3 OF 4

STANDARD SPECIFICATION – 2014 TRUCK, CAB & CHASSIS 55,000# - CONTINUED

TIRES: TYPE, WHEEL/TIRE SIZE

- ELEVEN (11) – HEAVY DUTY ACCURIDE 24.5” X 8.25”, POWDER COATED STEEL, HUB PILOTED, 0.472” DISC WHEELS WITH GUARDS F&R

- TEN (10) 11R24.5(H) TUBELESS RADIALS

- WHEEL WRENCH AND HANDLE

ACCEPTABLE BRAND TIRES

FRONT

- GOODYEAR G287 MSA OR MICHELIN XZY-3

REAR

- GOODYEAR G282 MSD OR MICHELIN XDS-2

FRAME

- HEAT TREATED ALLOY STEEL FRAME WITH MINIMUM YIELD STRENGTH OF 120,000 PSI AND MINIMUM SECTION MODULUS OF 20.6.

- 1 PIECE FULL DEPTH FRAME TO EXTEND A MINIMUM OF 12” BEYOND FRONT OF GRILLE

- AF-MINIMUM 48”

- BOTH OUTSIDE FRAME RAILS TO BE FREE OF OBSTRUCTIONS FOR TWENTY FOUR (24) INCHES BEHIND THE CAB FOUR TO ALLOW ROOM FOR MOUNTING A WING CABINET

- MINIMAL OBSTRUCTIONS FOR THE NEXT THIRTY (30) INCHES FOR PIPE BRACES

INSTRUMENTS/CONTROLS

- SPEEDOMETER, TACHOMETER, AMMETER/VOLT-METER, FUEL GAUGE (S), OIL PRESSURE GAUGE, TEMPERATURE GAUGE, AIR PRESSURE GAUGE WITH LOW PRESSURE WARNING

- ALL NECESSARY ELECTRICAL SWITCHES

- HOUR METER ACTUATED BY ENGINE OPERATION

- DASH MOUNTED AIR RESTRICTION INDICATOR

FUEL SUPPLY

- STAINLESS STEEL OR ALUMINUM TANK WITH STAINLESS STEEL STRAPS HAVING A MINIMUM CAPACITY OF 80 GALLON

- STEP TYPE FUEL TANK. NOT TO EXCEED 4” BEYOND REAR OF CAB

EXHAUST SYSTEM

- HORIZONTAL, VERTICAL  (OR COMBINATION) MUFFLER SYSTEM SHALL BE CONFIGURED NOT TO INTERFERE WITH PTO’S OR HYDRAULIC CABLES

- STACK (INCLUDING 90 DEGREE TURN OUT) MUST NOT EXTEND ABOVE TOP OF CAB AND NOT TO EXCEED 4” BEYOND REAR OF CAB

PAINT

- CLEAR COAT OMAHA ORANGE (DUPONT DULUX 93-082 OR EQUIVALENT) LEAD FREE

- NOTE:  SEE INDEPENDENT PAINT TESTING REQUIREMENTS AS PART OF THIS SPECIFICATION

RADIO/SPEAKERS (FACTORY)

- AM/FM WITH WEATHER BAND

SEATS-DRIVER/PASSENGER

- BUCKET, AIR SUSPENSION, HIGH BACK, HEAD REST, DRIVER’S ARM REST (RH) (NATIONAL CUSHION-AIRE OR EQUAL), HD CLOTH MORDURA, MILLIKEN (NGV) OR EQUAL.

FLOOR COVER

- VINYL WITH FACTORY RUBBER AUXILIARY MATS

LIGHTING, REQUIRED

- DAYTIME RUNNING, PRE-TRIP INSPECTION LIGHT TEST

MIRRORS, OUTSIDE RIGHT AND LEFT

- 6” X 15” EXTENDING TO 102” WITH A HEATED 7” CONVEX MIRROR

- PASSENGER SIDE “LOOK DOWN” CONVEX MIRROR

PAGE 4 OF 4

STANDARD SPECIFICATION – 2014 TRUCK, CAB & CHASSIS – 55,000# CONTINUED

BUMPERS -FRONT

- NONE REQUIRED

BACK UP ALARM

- ELECTRIC

HORN

  - AIR AND ELECTRIC – DUAL NOTE

TOW PACKAGE

  - TRAILER TOW PACKAGE SHALL BE PROVIDED AND INCLUDE TRAILER LIGHT PACKAGE, HAND OPERATED CONTROL VALVE, AND AIR LINES TO REAR OF FRAME

SOFTWARE

- DIAGNOSTIC SOFTWARE AND ALL REQUIRED LAPTOP COMPUTER CABLES AND OR CONNECTIONS FOR DIAGNOSIS OF ENGINE (INCLUDING KEY ON AND KEY OFF TEST, CYLINDER CUT OUT TEST, INJECTOR DISABLE TEST), CHASSIS & ELECTRICAL SYSTEM, AND ABS SYSTEM. LATEST VERSION OF ALLISON TRANSMISSION SOFTWARE SHALL BE PROVIDED FOR PROGRAMMING WITH ONE DAY ON SITE (DOT) PROGRAMMING INSTRUCTION. ALL SOFTWARE TO INCLUDE FREE UPDATES AND RENEWALS OF ALL SUBSCRIPTIONS FOR A PERIOD OF TEN (10) YEARS BEYOND MODEL YEAR. THIS SPECIFICATION SHALL REQUIRE A QUANTITY OF NINE (9 EACH) COMPLETE SETS OF THE ABOVE SOFTWARE BE SUPPLIED AND DELIVERED TO NHDOT MECHANICAL SERVICES AS PART OF THIS SOLICITATION AND INCLUDED IN THE UNIT COST

SYSTEMS CALIBRATIONS

  - UPON FINAL AWARD, THE SUCCESSFUL VENDOR WILL PRESENT A COMPLETE LIST OF DEFAULT ENGINE, ELECTRICAL, FUEL AND TRANSMISSION SYSTEM CALIBRATIONS FOR REVIEW AND ADJUSTMENT WITH THE END USER

SERVICE AND PARTS MANUALS

- FOR THE LIFE OF THE VEHICLE (S), THE AWARDED BIDDER SHALL PROVIDE WEB BASED ACCESS TO ALL TRUCK-SPECIFIC SERVICE MANUALS, TECHNICAL SPECIFICATIONS AND PARTS CATALOGS FOR A MINIMUM OF ELEVEN (11) NHDOT VEHICLE MAINTENANCE LOCATIONS.

APPLICATION:	THIS SPECIFICATION COVERS THE STATE OF NEW HAMPSHIRE’S MINIMUM REQUIREMENT FOR A VOCATIONAL CAB & CHASSIS, INTENDED FOR THE SOLE PURPOSE OF PLOWING, SANDING AND OTHER HIGHWAY MAINTENANCE OPERATIONS. TO FACILITATE THE MOUNTING OF PLOW EQUIPMENT, AMPLE SPACE MUST BE AVAILABLE FOR LEFT AND RIGHT POWER TAKE OFFS. CLEAR SPACE BENEATH AND TO THE REAR OF THE CAB FOR HYDRAULIC CABLES AND WING CABINET.  ALL EXPOSED CONNECTIONS SHALL BE SEALED AND 100% WATER TIGHT.  THE MANUFACTURER WILL BE SOLELY RESPONSIBLE FOR MEETING THIS REQUIREMENT.