State of New Hampshire                                                                                                        October 16, 2013

Page 1 of 3

POWER TILT PLOW HITCH & HYDRAULICS         DOUBLE WING

SCOPE:

- Complete power hydraulics (see notes) for reversible plow and double wing, including front power tilt lifting device and push frame

- Hydraulic wing cabinet with minimum 43” lifting capacity

- Parallel push arms, front wing slides, oil reservoir with a minimum 40 gallon capacity with magnetic drain plug

- Provisions for oil level sensor and a Hydro-Craft HSG-55 6” sight level/temperature gauge (mounted facing cab)

- REXROTH Model M4-12 valves and cab controls for operating two-way front plow, right and left hand wing tower slides, right and left, front and rear wing cables, dump body, spreader conveyor & spinner

- All Grade 8 fasteners shall be furnished

HITCH:

- Front hitch shall be designed to fit chassis designated by the state without modification, drilling or welding

- The hitch shall be equipped with a hydraulic tilt utilizing 4” X 10” plow lifting cylinder, and must be fully detachable

- Plow lift arm assembly designed to withstand 2500 psi to relief without fracture

- Pins used for tilt or removal of hitch to be equipped with handles

- Plow light and license plate brackets shall be installed and designed to minimize vibration

- When tilted or detached, a plate bracket and channel/angle iron bumper with non-skid step shall remain with truck.  Sufficient clearance to prevent cab contact shall be provided when tilted

- Cable over the cab will not be accepted.  Full trip hinge not acceptable.

- “D” Hinge shall have a 1-1/2”X 6” bolt to attach wing

- Three (3) holes for plow mounting pins shall be provided with bottom hole 16” O.C. from ground

- All ½” wire rope thimbles to be HEAVY DUTY Campbell part number 626-0205 or equal

HYDRAULIC CONTROLS:

- Hydraulic cabinet shall be either American Snow Plows “P” Series, Viking “H” series or H.P.F. “DTH-CL” Series - NO SUBSTITUTES

- Valves shall be enclosed in a 12” deep cabinet centered directly behind cab and stacked in the following order from left to right:  END CAP, PLOW LIFT,  PLOW REVERSE,  LH WING TOE,  LH WING HEEL,  DUMP BODY HOIST, INLET, LH WING SLIDE,  RH WING TOE,  RH WING HEEL,  RH WING SLIDE,  SPINNER, CONVEYOR, END CAP

- The REXROTH valve configuration shall be:

- END CAP:  BLANK  #255157

- PLOW LIFT: M4-12-2X/SZZZE045-040AZZZ-S  #243832 DA

- PLOW REVERSE:  M4-12-2X/SZZZE061-061AZZZ-S  #266330 DA

- LH WING TOE: M4-12-2X/SBMQE000-044AZZZ-S  #263071 SA

- LH WING HEEL:  M4-12-2X/SBMQE000-044AZZZ-S  #263071 SA

- DUMP BODY HOIST:  M4-12-2X/SBMQE000-130AZZZ-S  #243839 SA

- INLET:  OPEN CENTER  #248041

- LH WING SLIDE:  M4-12-2X/SZZZE061-061AZZZ-S  #266330 DA

- RH WING TOE:  M4-12-2X/SBMQE000-044AZZZ-S  #263071 SA

- RH WING HEEL:  M4-12-2X/SBMQE000-044AZZZ-S  #263071 SA

- RH WING SLIDE:  M4-12-2X/SZZZE061-061AZZZ-S  #266330 DA

- SPINNER:  M4-12-2X/SZZZJ000-030W23-ZZ-S  #244546

- CONVEYOR:  M4-12-2X/SZZZJ000-057W23-ZZ  #244552

- END CAP: “Q” #248148

State of New Hampshire                                                                                                        October 16, 2013

Page 2 of 3

POWER TILT PLOW HITCH & HYDRAULICS         DOUBLE WING                                                    (Continued)

- Valve stack shall be mounted 5” from bottom of spools to bottom of cabinet

- One additional hole for dual remote control of the plow lift spool shall be located directly behind the standard plow lift cable hole

- Locations of lower holes for welded pipe nipples for spreader hydraulics, suction and return lines shall be supplied by the State to successful vendor

- Cabinet doors shall be equipped with handles protruding a maximum of 2” for ease of removal

HYDRAULIC RESERVOIR:

- A minimum 40 gallon reservoir shall be provided and mounted directly behind cab, at least 6” above valve enclosure for access to bottom fittings

- A gate valve shall be provided and installed in the suction port of the tank.  Corresponding holes through valve enclosure shall be provided

- A 1-1/2” NPT suction port in tank shall be located 9” O.C. from left side of hydraulic valve enclosure

- Tank shall also include a magnetic drain plug

- A1/4” NPT “P” Line port

- A Hydro-Craft HSG-55 6” sight level/temperature gauge, located facing cab

- Inside of reservoir shall be clean of all scale and debris

- A 1” NPT connection shall be provided at the top center of tank (and plugged to prevent contamination during delivery) for installation of a Byers E22 Oil Level Sensor Kit, supplied and installed by the State

- Suction and “P” line ports shall extend into cabinet at least 1” from bottom.

- A Parker-Hanifin P50ATDD25C15PSINN filter assembly w/bypass shall be provided with a 1 ¼” NPT brass ball valve

- All cylinders shall be Mailhot, double acting and accept S.A.E. #8 Boss “O” Ring fittings

- Cylinders shall be nitrided twice, shall utilize U-Cup type seals and shall be designed for working pressures to 4,000 p.s.i.  All cylinders shall be warranted for two (2) years from in service date (determined by the state)

- Wire rope cable shall be ½” (8 X 19 IPS)

- All sheaves shall be equipped with graphited bronze bushings

- All pins shall be equipped with grease fittings

- Cabinet shall be equipped with access holes & covers for grease fittings

OPERATOR CONTROLS:

- Hydraulic valves to be controlled from inside the cab by remote cable control

- Nine (9) stackable control levers supplied shall be AREN/QUADCO C80 Series Modular Controls.  Four (4) levers shall be Model #C8522B000, Four (4) levers shall be Model # C8523B000 and one (1) lever shall be Model #C8521B000. One Gressen or equal handle assembly, part # K-20-VH-B with 5/16-24 yoke for remote plow frame tilt.

MSDS’s:

- Manufacturer shall supply two (2) complete sets of Material Safety Data Sheets for all construction and coating materials used in both the construction and finishing of the equipment furnished. MSDS sheets must be received before or at time of first delivery of components.

NOTE(S):

Operator control cables and all hydraulic hoses, fittings and piping will be furnished by the State and is not a part of this specification unless otherwise noted.

If hydraulic systems are requisitioned to fit different chassis models, the systems shall be marked accordingly when delivered.

State of New Hampshire                                                                                                        October 16, 2013

Page 3 of 3

POWER TILT PLOW HITCH & HYDRAULICS         DOUBLE WING                                                    (Continued)

Each plow frame delivered shall be shipped attached to a metal stand that will support the plow frame vertically and have provisions for handling with a forklift.  Stands will be available for pick up by vendor after plow frames are installed.

PAINT:

- Equipment to be primed and painted Omaha Orange, both LEAD FREE.

NOTE:  SEE INDEPENDENT PAINT TESTING REQUIREMENTS AS PART OF THIS SPECIFICATION

Equipment to be mounted by others.